## Slide 1
W.L. Li1, N. Guo1, Z.X. Yang1, T. Helfer2
1 Zhejiang University
2 CEA
25 November 2020
Implementing a shear-transformation-zone model in MPM and SPFEM using MFront

## Slide 2: Where are we?
ZJU is located in Hangzhou.
Historical city that blends the classic and modern elements of China
Famous for sightseeing and e-commerce
Host of the 2022 Asian Games

## Slide 3: Outline
Shear-transformation-zone (STZ) model
MFront implementation and MTest
Interfacing NairnMPM via MFrontGenericInterfaceSupport
Applications
Granular column collapse, footing settling on soft ground
Interfacing SPFEM in Python via mgis.behaviour
Discussion

## Slide 4
(Falk and Langer, 1998)
Closeup of shear transformation zone before
and after undergoing transformation
Simulation of a bubble model in 2D
undergoing oscillatory shear strain
(Lundberg et al., 2007)
The STZ theory attributes plastic deformation to irreversible, local granular rearrangements occurring at loose spots, known as STZs.
Basic idea of STZ theory
Model introduction

## Slide 5
(Ma and Elbanna, 2018)
Plastic strain rate:
Evolution:
A non-equilibrium thermodynamics framework
Formulation
STZ flipping rate:
State parameter: compactivity

## Slide 6
Implementation

## Slide 7
Symbol | Description | Value | Remark
 | Young’s modulus | 40 MPa | Typical range for sand: 10 MPa – 100 MPa
 | Poisson’s Ratio | 0.3 | Typical range: 0.2 – 0.45
 | Cohesion | 0.0 | Cohesionless sand
 | Frictional coefficient | 0.5 | Typical value for loose to medium-dense sand ()
 | Particle Density | 2650 kg/m3 | Typical density of silica
 | Plastic strain increment per STZ | 1.0 | Corresponding to a particle sliding a distance equal to its diameter
 | Effective volume expansion coefficient | 0.025 | Corresponding to 0.3% volumetric plastic strain at the steady state
 | Effective volume capacity | 0.025 | Controlling the evolution rate of
 | Steady state compactivity | 0.08 | Material parameter that can be fitted from the steady state response
 | Initial compactivity | 0.04 | Material parameter that depends on the initial condition (e.g. density and stress)
 | Grain size | 0.1 mm | Typical sand grain size
 | Excess volume per STZ in units of grain volume | 1.0 | Activation volume is about the average grain volume
Symbol | Description | Value | Remark
 | Young’s modulus | 40 MPa | Typical range for sand: 10 MPa – 100 MPa
 | Poisson’s Ratio | 0.3 | Typical range: 0.2 – 0.45
 | Cohesion | 0.0 | Cohesionless sand
 | Frictional coefficient | 0.5 | 
 | Particle Density | 2650 kg/m3 | Typical density of silica
 | Plastic strain increment per STZ | 1.0 | Corresponding to a particle sliding a distance equal to its diameter
 | Effective volume expansion coefficient | 0.025 | Corresponding to 0.3% volumetric plastic strain at the steady state
 | Effective volume capacity | 0.025 | 
 | Steady state compactivity | 0.08 | Material parameter that can be fitted from the steady state response
 | Initial compactivity | 0.04 | Material parameter that depends on the initial condition (e.g. density and stress)
 | Grain size | 0.1 mm | Typical sand grain size
 | Excess volume per STZ in units of grain volume | 1.0 | 
Model parameters

## Slide 8
Biaxial shear tests subjected to different strain rates
Model performance

## Slide 9
Compared with model
Model performance

## Slide 10
NairnMPM
MfrontGenericInterfaceSupport (MGIS)
NairnMPM is an open-source platform for the material point method (MPM) simulations written in object-oriented C++. The code is developed and maintained by Prof. J.A. Nairn at the Oregon State University. Parallel computation is achieved in the code.
(Tan and Nairn, 2002)
MGIS is an MFront project developed to provide bindings to other programming languages for the constitutive models implemented by MFront. The available bindings available currently include Python, Julia, Fortran 2003 and C/C++.
(Helfer et al., 2020)
Interfacing NairnMPM

## Slide 11
Computational cycle for one timestep in MPM
Map from material points to nodes
  Compute nodal mass
  Compute nodal momentum
  Compute nodal velocity
P2G
Update deformation and stress of material points
  Compute material point strain increment
  Update material point strain
  Transfer strain increment and state variable to MGIS
  Update stress and state variable information using MGIS
  Transfer updated stress and state variable back to NairnMPM
Solve momentum equation
  Compute internal force ad external force
  Compute total nodal force
  Update nodal momentum
Map from nodes to material points
  Update particle velocity
  Update particle position
G2P
Interfacing NairnMPM

## Slide 12
Coupling NairnMPM and MGIS
Using MGISBehaviourHandler to
load Behaviour object b
Using BehaviourData d to store state
information of an integration point
Recover the state information
of a material point at last step
Retrieve updated state information from
BehaviourData and transfer back to NairnMPM
Set material property and initialize
state information of STZ model
Using Integrate to update state
information for given strain increment
MGIS engine
Interfacing NairnMPM
NairnMPM
MGIS
Loop over all material points

## Slide 13
Verification of the coupling
Biaxial shear tests subjected to different strain rates
Interfacing NairnMPM

## Slide 14
Granular column collapse
Geometric and material parameters following Nguyen et al. (2017)
Application

## Slide 15
Application
Flow animation

## Slide 16
Compared with experiment
Application

## Slide 17
Application
Footing settling on soft ground

## Slide 18
Application
Animation and load-settlement curve

## Slide 19
Interfacing SPFEM in Python

## Slide 20
Interfacing SPFEM in Python
Application animations
Granular column collapse
Granular silo discharge

## Slide 21
Discussion
Parallel computing
Multiple materials
Adding/removing data points
Mesh interpolation

## Slide 22
Thank you!